## Slide 1: Crook County Transportation System Plan
Board Hearing
October 1, 2025

## Slide 2: Agenda
Transportation System Plan (TSP) Overview
Existing Issues and Needs
Proposed Transportation System Improvements
Funding and Implementation
Discussion
Next Steps

## Slide 3: Planning Commission Role
Review key outcomes of draft TSP
Advise on TSP alternatives and recommendations
Recommend TSP to Board of Commissioners

## Slide 4: TSP Overview
Introduction to the city of Harrisburg TSP UPDATE

## Slide 5: What Is a TSP?
Addresses transportation needs for all modes of travel now and for the next 20 years
Prioritizes projects and helps County comply with state rules
Special focus on:
  Enhancing connectivity and improving safety for all modes of travel.
  Addressing safety issues in areas of congested concern like Powell Butte.
  Developing near-term options for emergency access of Juniper Canyon area.
Updating Crook County’s 2017 TSP

## Slide 6: Why are we updating the TSP now?
Growth in the county and surrounding areas has outpaced projections.
Increased demand on the transportation system has increased need to advance projects sooner and evaluate new solutions.
Safety for all modes of travel and increased connectivity are an important focus.
The TSP Update is a focused update to explore these issues.

## Slide 7: What Is a TSP?
Goals and objectives to guide process
Prioritize projects and programs
Funding options
Compliance with state rules

## Slide 8: Decision-Making Process

## Slide 9: Project Timeline

## Slide 10: TSP Goals
Mobility and Connectivity
Economic Development
Safety
Multimodal Users
Environment
Planning and Funding
Equity

## Slide 11: Engagement
Introduction to the city of Harrisburg TSP UPDATE

## Slide 12: Engagement Activities
Project Advisory Committee– 2 total meetings
Milestone #1 – February 2024
  In-person open houses, survey, and open comment form
Milestone #2 – October – November 2024
  In-person open houses, survey, and open comment form
Milestone #3 – April – May 2025
  In-person public meeting, open house, survey, and email responses
August 2025 – Juniper Canyon Meeting

## Slide 13: Engagement Feedback
More than 500 people attended events, responded to surveys, and shared input
Transportation Safety is the top community priority
Top Project Priorities:
  SW Powell Butte Hwy and OR 126 intersection
  Juniper Canyon Access
Notes:   Significant interest in building projects as soon as possible
  Strong desire to reduce speeding, improve enforcement
  Limited community support for new funding sources that would increase costs for residents

## Slide 14: Engagement Feedback
More than 90% of participants confirmed projects align with community priorities
Other Key Findings:
  Significant interest in building projects as soon as possible
  Strong desire to reduce speeding, improve enforcement
  Limited community support for new funding sources that would increase costs for residents

## Slide 15: Needs and Issues
Introduction to the city of Harrisburg TSP UPDATE

## Slide 16: Needs and Issues
Significant growth has outpaced previous projections, including Powell Butte, Juniper Canyon, Brasada Ranch, and data center traffic.
Growth is resulting in increased traffic speeds, volumes, and safety concerns
Only one way to reach Juniper Canyon limits access and emergency response, impacts traffic

## Slide 17: Recommended Improvements

## Slide 18: ROADWAY AND INTERSECTION IMPROVEMENTS
Intersection and Operations Improvements
Access Management
Bridge Improvements

## Slide 19: Project R-1A: OR 126 and SW Powell Butte Highway
Key issues:
Recommended Alternative: Single-lane roundabout
  Maintains turning movements
  Reduces turning conflicts.
  Reduces traffic delays in the near term.
  Provides easier navigation of intersection.
  Expected to cost less than dual lane roundabout.
  Cost: $3,400,000

## Slide 20
Project R-1A: OR 126 and SW Powell Butte Highway
Solution: Single-lane roundabout
  Maintains turning movements
  Reduces turning conflicts.
  Reduces traffic delays in the near term.
  Provides easier navigation of intersection.
  Expected to cost less than dual lane roundabout.
  Cost: $3,400,000
Notes: Safety – collisions at this intersection
Post office access
Delays for turning vehicles
Intersection is forecast to not meet ODOT’s standard for congestion

## Slide 21: Roundabouts – how do they improve safety and congestion?
Designed to slow entering traffic (20MPH or less)
Reduce congestion by allowing better vehicle throughput
  Often better than signals
Reduce conflict points = improved safety
Lower operations/maintenance cost
Designed for large vehicles/trucks/trailers

## Slide 22: Project R-2: OR 126 and SW Williams road
Key issues
Intersection is forecast to not meet ODOT’s standard for congestion
School, other destinations at this intersection
Speeding and safety
Solution: Single-Lane Roundabout
  Improves safety performance for all modes
  Provides traffic calming
  Cost: $3,400,000

## Slide 23: Project JC-1 and JC-2: Juniper Canyon Access
Key Issues:
Juniper Canyon community is growing; in recent years, ~50 new housing units / year
One main access road – limits:
  Options if route is closed
  Emergency response
  Evacuation routes
Increased congestion through Prineville

## Slide 24
Cost Estimates
Cost estimates are “planning-level,” based on limited information and assumptions
Greater design detail = greater cost certainty
These estimates have substantial contingency and -30%/+50% range to account for uncertainty

## Slide 25: Project JC-1: Juniper Canyon Access
Solution: W01
  Previously vetted alternative
  Helps relieve congestion along SE Juniper Canyon Road.
  Provides additional travel options for emergency response.
  Cost: $6,090,000 to $13,050,000

## Slide 26: Project JC-2: Juniper Canyon Access
Solution: E10
  Gravel roadway – provide emergency evacuation route
  Located primarily on BLM land
  Cost: $24M to $52M

## Slide 27
Key issues:
Current configuration is skewed, limited sight distance
Difficult turning movements from SE Juniper Canyon Road
Intersection is forecast to not meet ODOT’s standard for congestion
Solution: Realign intersection, acceleration lanes
Improves intersection safety
Retains existing movements, would accommodate farm/freight vehicles
Reduces conflict points
Reduces traffic congestion
Cost: $2,100,000
Project R-4: SE Juniper Canyon Road and OR 380

## Slide 28: Project R-3: OR 126 and SW Parrish Lane
Key issues:
Intersection is forecast to not meet ODOT’s standard for congestion
No dedicated left turn lane to access SW Parrish Lane
Solution: Widen OR 126 from SW Valley View Road to Stillman Road and include center two-way left turn lane
Reduces traffic congestion and delay
Opportunity to add medians/physical markers to encourage slower driving
Cost: $900,000
Notes: Expected to exceed mobility targets in future no build higher growth scenario
Analysis of future traffic conditions shows that this location would meet turn lane warrants.

## Slide 29
Widen OR 126 and include center two-way left turn lane

## Slide 30: Bridges
Replace
SW Powell Butte Highway over Powell Butte Canal
SW Powell Butte Highway over Powell Butte Wasteway
Johnson Creek Road NE over Ochoco Main Canal
Continue
Non-NBI bridge replacement program
  Replace one non-NBI bridge per year
Study
Repairing or replacing County Road 221 bridge over Paulina Creek

## Slide 31: Roadways and Intersections
Access Improvements
OR 126 at:
  Kissler Rd
  Copley Rd
  Minson Rd
  Yates Rd
  Wiley Rd
New Roadway
Preferred Alignment: W01
Operations Improvements
OR 126 & PB Hwy
OR 126 & Williams Rd
OR 126 & Parrish Ln
Juniper Canyon Rd & OR 380

## Slide 32: Safety IMPROVEMENTS
Projects address:
  Locations with higher-than-expected crash rates
  Community input
  2017 TSP Safety Improvements
Notes:   Visibility and awareness
  Roadway / curve navigation
  ODOT standards
  Speeding
  Crashes / roadway departures
  Nighttime driving and inclement weather
  Potential conflicts

## Slide 33
PROJECT S-1: S POWELL BUTTE HWY AND SW BUSSETT ROAD
Solution: Realign intersection and install acceleration lanes
Improves visibility and awareness. Simplifies travel patterns.
Responds to and mitigates inclement weather conditions and associated safety challenges.
Reduces roadway departure crashes.
Cost: $870,000
Notes: Key issues:
Exceeds critical crash rate
Poor visibility
High travel speeds

## Slide 34: Safety IMPROVEMENTS
S Powell Butte Highway and SW Bussett Road
Rimrock Acres Loop and OR 370
S Powell Butte Highway and Alfalfa Road
OR 126 east of SW Powell Butte Highway to Copley Road
OR 370 east of Happy Hollow Drive
OR 380 south of NE 3rd Street
SE Juniper Canyon Road (S-7, S-8, S-9)
S Powell Butte Highway
SE Davis Loop
OR 126 (S-12, S-15)
US 26
NW Lamonta Road

## Slide 35: SAFETY IMPROVEMENTS
Treatment | Benefit or Impact | Example Location
Rumble strips, raised pavement markings, or edge line striping | Improves visibility and awareness Enhances roadway navigation | OR 126
Curve chevrons or guardrail | Improves visibility and awareness Reduces roadway departure crashes | Rimrock Acres Loop and OR 370
Variable speed limits | Responds to inclement weather | SE Juniper Canyon Road
Speed feedback signs* | Improves awareness. Encourages speeding drivers to slow down. | OR 126
Lighting | Improves visibility and awareness | S Powell Butte Highway and Alfalfa Road
Remove trees in clear zone | Reduces fixed-object crashes with trees | Davis Loop
*Requires coordination with/approval by ODOT when on state route

## Slide 36: ACTIVE TRANSPORTATION IMPROVEMENTS
Install sidewalks, curb, gutter, curb ramps, lighting, marked crosswalks
OR 126 and SW Williams Road
Install shared-use path
OR 126 from SW Powell Butte Highway to Prineville UGB
Barnes Butte Road to Iron Horse path
US 26 from existing path to County line
Houston Lake Road, SW Williams Road, Reif Road
OR 27 to planned path in Prineville

## Slide 37: ACTIVE TRANSPORTATION IMPROVEMENTS
Add paved shoulders
Barnes Butte Road
SE Juniper Canyon Road
Construct bicycle hub (rest stop)
OR 27 Scenic Bikeway corridor
Add bicycle route signage
Countywide
Notes: Construct a bicycle hub, or "rest stop," for hikers, bicyclists, recreationalists, and community members along the OR 27 scenic bikeway corridor; provide small shelter, information kiosk (map/community calendar), bicycle tool station, and bench/sitting area.

## Slide 38: Public transportation Improvements
Project Descriptions | 
Cascades East Transit Service Enhancement Plan | Institute evening and Saturday limited circulation as part of Route 26 flex-route
Fixed route enhancements | Increase service in Prineville with eventual deviated fixed route or a purely fixed route to provide connections to more destinations.
Dial-A-Ride enhancements and Transportation Network Company (TNC) encouragement | Improve accessibility for residents in rural Crook County through a larger service area for dial-a-ride service. Additionally, incorporate TNC elements into the current Dial-A-Ride system.
Transit community outreach | Educate the community about connections available within Redmond and Prineville to reach key destination such as Central Oregon Community College (COCC), the Redmond Airport, the hospital, and additional locations within Bend.

## Slide 39: Freight
Project Location | Project Description
Bus Evans Road and Elliott Lane reconstruction to freight route standards | Reconstruct Bus Evans Road and Elliot Lane to freight route standards, with 12-ft lanes, 2-ft shoulders on each side, including 17.14 feet of rock shoulder, and the appropriate roadway base. Bus Evans Road and Elliott Lane reconstruction to freight route standards
US 26 railroad bridge feasibility study | Conduct a feasibility study regarding the reconstruction of the US 26 railroad bridge or lowering of OR 126 to accommodate oversized loads on US 26.

## Slide 40: Related Prineville TSP projects

## Slide 41: Overview
Prineville completed their TSP update earlier this year
Includes a number of projects that improve east-west connections
Major investment proposed in West Y
New street connections that take pressure of 3rd Street

## Slide 42: West Y
Roundabout concept to address safety, congestion issues
Would increase overall throughput of OR 126/3rd Street
Notes: Would reconfigure ramps today that don't oeprate well today and is expected to operate very poorly in future.

## Slide 43: O’Neil Highway
Intersection reconfiguration to reduce turning crashes
Would handle increased traffic volumes better
Notes: High volumes of left turns
Crashes with someone turning right, car going around and hit left turning vehicle.

## Slide 44: Other Projects
Widen Combs Flat between Lynn and 3rd Street to arterial standards
Lynn/Combs Flat intersection: near term - lighting, signage, site distance improvements
  Long term: intersection control evaluation

## Slide 45
Notes: Intended to take pressure off of 3rd with Peters Road and Combs Flat extensions.
R-1 9th street connection – offering more opportunities to link to regional connections.
Signal upgrades ODOT tie in signals on 3rd.
Access mgmt strategy that would consolidate driveways in the future to reduce turning conflicts.
Cyclists on 2nd/4th (parallel routes)

## Slide 46: New connections
New connections to Lamonta, US 26, recently completed Combs Flat Extension
9th Street extension
All reduce traffic on 3rd Street

## Slide 47: TSP Projects Summary
Projects organized by priority

## Slide 48: TSP Projects Summary
Project ID | Project Name/Location | Improvement Time Frame | Cost Estimate | Possible Funding Source
R-3A | OR 126 & SW Parrish Ln: Widen OR 126 from SW Valley View Rd to Stillman Rd (center two-way left-turn lane). | Near | $900,000 | ODOT, Local Funds
JC-1 | Juniper Canyon Access: Develop new roadway connection in Juniper Canyon between Davis Loop and OR 27. | Near | $9,300,000 to $20,000,000 | Local Funds, Grants
JC-2 | Juniper Canyon Access: Develop new gravel roadway connection in Juniper Canyon between SE Simpson Rd and OR 380 | Near | $24,000,000 to $52,000,000 | Local Funds, Grants

## Slide 49: TSP Projects Summary
Project ID | Project Name/Location | Improvement Time Frame | Cost Estimate | Possible Funding Source
S-3A | S Powell Butte Hwy & Alfalfa Rd: Install lighting and curve chevrons along S Powell Butte Hwy. Reassess curve warning signage and check for sign spacing. | Near | $71,000 | Local Funds, Grants
S-4 | OR 126 east of Powell Butte Hwy to Copley Rd: Widen edge line striping. | Near | $260,000 | ODOT
S-5 | OR 370 east of Happy Hollow Dr: Install rumble strips and/or wider edge line striping. | Near | $22,000 | ODOT

## Slide 50: TSP Projects Summary
Project ID | Project Name/Location | Improvement Time Frame | Cost Estimate | Possible Funding Source
S-6 | OR 380 south of NE 3rd St: Evaluate access management along the corridor. | Near | N/A | ODOT
S-7 | Juniper Canyon Rd variable speed limit: Implement variable speed limit based on weather conditions. | Near | TBD based on future evaluation | Local Funds
S-8 | Juniper Canyon Rd alignment delineation: Add raised pavement markers on SE Juniper Canyon Rd. Add edge-line rumble strips to SE Juniper Canyon Rd. | Near | $94,000 | Local Funds

## Slide 51: TSP Projects Summary
Project ID | Project Name/Location | Improvement Time Frame | Cost Estimate | Possible Funding Source
S-9 | Juniper Canyon Rd Add or enhance horizontal curve signage and markings. | Near | $10,000 | Local Funds
S-10 | Powell Butte Rd Add or enhance horizontal curves pavement markings. | Near | $10,000 | Local Funds
T-3 | Dial-a-ride enhancements and transportation network company encouragement. | Near | Already adopted as part of other plans. | 
T-4 | Transit community outreach. | Near | Variable | ODOT City of Prineville Local Funds

## Slide 52: TSP Projects Summary
Project ID | Project Name/Location | Improvement Time Frame | Cost Estimate | Possible Funding Source
R-1A | OR 126 & Powell Butte: Construct a single‑lane roundabout. | Medium | $3,400,000 | ODOT, Development, Local Funds
R-2A | OR 126 & SW Williams Rd: Construct a single-lane roundabout. Requires an Intersection Control Evaluation to determine appropriate traffic control change. | Medium | $3,400,000 | ODOT, Safe Routes to School, Local Funds
R-5 | OR 126 at Kissler Rd. Balance destination access with mobility and safety of the transportation system. | Medium | $20,000 | ODOT
R-6 | OR 126 at Copley Rd. Balance destination access with mobility and safety of the transportation system. | Medium | $20,000 | ODOT

## Slide 53: TSP Projects Summary
Project ID | Project Name/Location | Improvement Time Frame | Cost Estimate | Possible Funding Source
R-7 | OR 126 at Minson Rd. Balance destination access with mobility and safety of the transportation system. | Medium | $20,000 | ODOT
R-8 | OR 126 at Yates Rd. Balance destination access with mobility and safety of the transportation system. | Medium | $20,000 | ODOT
R-9 | OR 126 at Wiley Rd. Balance destination access with mobility and safety of the transportation system. | Medium | $20,000 | ODOT
BR-1 | County Road 221 bridge over Paulina Creek (NBI Bridge 19083): Study cost of repairing or replacing this functionally obsolete bridge. | Medium | $30,000 | Local Funds, Grants

## Slide 54: TSP Projects Summary
Project ID | Project Name/Location | Improvement Time Frame | Cost Estimate | Possible Funding Source
BR-2 | SW Powell Butte Hwy bridge over Powell Butte Canal (NBI Bridge 03291): Replace bridge. | Medium | $1,500,000 | Grants
BR-3 | SW Powell Butte Hwy bridge over Powell Butte Wasteway (NBI Bridge 03293): Replace bridge. | Medium | $1,500,000 | Grants
BR-4 | Johnson Creek Rd NE bridge over Ochoco Main Canal (NBI Bridge 13C06A): Replace bridge. | Medium | $1,500,000 | Grants
BR-5 | Non-NBI bridge replacement program: Replace one non-NBI bridge per year. | Medium | $4,500,000 | Local Funds

## Slide 55: TSP Projects Summary
Project ID | Project Name/Location | Improvement Time Frame | Cost Estimate | Possible Funding Source
S-2 | Rimrock Acres Loop & OR 370: Install lighting. Install raised pavement markings. Evaluate existing curve warning signage locations and warning speeds. Install curve chevrons, guardrail, and rumble strips. | Medium | $180,000 | Local Funds, Grants
S-11 | Davis Loop Rd Remove trees within clear zone. | Medium | TBD based on future study | Local Funds
S-12 | Powell Butte (OR 126) Install/maintain speed feedback signs. | Medium | $50,000 | ODOT

## Slide 56: TSP Projects Summary
Project ID | Project Name/Location | Improvement Time Frame | Cost Estimate | Possible Funding Source
S-13 | US 26 Add systemic safety treatments, including edgeline rumble strips. | Medium | $50,000 | ODOT
S-14 | Lamonta Rd Install horizontal curve signage, speed feedback sign, and delineators. | Medium | $50,000 | Local Funds
S-15 | OR 126 Install systemic safety treatments, including edgeline and centerline rumble strips. | Medium | $50,000 | ODOT

## Slide 57: TSP Projects Summary
Project ID | Project Name/Location | Improvement Time Frame | Cost Estimate | Possible Funding Source
B-1 | OR 126 from SW Powell Butte Hwy to Prineville urban growth boundary: Add shared-use trail along the south side of OR 126. | Medium | $6,600,000 | ODOT, Local Funds
B-8 | OR 27 Add shared-use trail to connect to planned path in Prineville. | Medium | $4,400,000 | ODOT, Local Funds
B-9 | Countywide Add bicycle route signage. | Medium | $50,000 | Local Funds

## Slide 58: TSP Projects Summary
Project ID | Project Name/Location | Improvement Time Frame | Cost Estimate | Possible Funding Source
P-1A | OR 126 and SW Williams Rd: Install sidewalk, curb and gutter, curb ramps, and intersection lighting. Install marked crosswalks on all four legs of the intersection. | Medium | $2,900,000 | ODOT, Local Funds, Sidewalk Improvement Program
T-1 | Crook County Service Enhancement Plan: Institute evening and Saturday limited circulation as part of Route 26 flex route. | Medium | Already adopted as part of other plans. | 
F-2 | US 26 railroad bridge feasibility study. | Medium | $35,000 | ODOT

## Slide 59: TSP Projects Summary
Project ID | Project Name/Location | Improvement Time Frame | Cost Estimate | Possible Funding Source
R-4A | SE Juniper Canyon Rd & OR 380: Realign intersection with left acceleration lane. | Long | $2,100,000 | Local Funds
S-1 | S Powell Butte Hwy & SW Bussett Rd: Install rumble strips along the curve. Implement variable speed limits that lower in icy conditions. Install lighting. Reassess curve warning signage and check sign spacing. Install acceleration lanes on S Powell Butte Hwy. Reconstruct intersection to simplify circulation patterns and turning movements. | Long | $870,000 | Local Funds, Grants

## Slide 60: TSP Projects Summary
Project ID | Project Name/Location | Improvement Time Frame | Cost Estimate | Possible Funding Source
B-2 | Barnes Butte Rd: Add paved shoulder to Barnes Butte Rd. | Long | $3,800,000 | Local Funds
B-3 | Barnes Butte Shared-Use Trail Connections: Add shared-use trail connecting Barnes Butte Rd to Iron Horse shared-use trail in Prineville. | Long | $4,900,000 | Local Funds
B-4 | OR 27 Scenic Bikeway Bicycle Hub. Construct a bicycle hub, or "rest stop," for hikers, bicyclists, recreationalists, and community members along the OR 27 scenic bikeway corridor; provide small shelter, information kiosk (map/community calendar), bicycle tool station, and bench/sitting area. | Long | $30,000 | Private Partnership

## Slide 61: TSP Projects Summary
Project ID | Project Name/Location | Improvement Time Frame | Cost Estimate | Possible Funding Source
B-5 | US 26 (Madras Highway) shared-use trail: Extend existing shared-use trail northwest to the county line parallel to US 26. | Long | $7,100,000 | ODOT, Local Funds
B-6 | Houston Lake Rd, SW Williams Rd, and Reif Rd Add shared-use trails. | Long | $10,500,000 | Local Funds
B-7 | Juniper Canyon Rd (south) Add paved shoulders. | Long | $5,400,000 | Local Funds

## Slide 62: TSP Projects Summary
Project ID | Project Name/Location | Improvement Time Frame | Cost Estimate | Possible Funding Source
T-2 | Fixed-route enhancements to increase service in Prineville and expand connections to destinations. | Long | TBD | CET City of Prineville Local Funds
F-1 | Bus Evans Rd and Elliott Ln. | Long | $15,000,000 | Local Funds Grants

## Slide 63
Funding and Implementation

## Slide 64: Project Costs (2024 $)
Total TSP Project Costs: $112.9 million
  Projects in partnership with ODOT: $27.5 million
  Locally-led projects: $85.4 million
County has no dedicated source of funding for transportation.
  New funding sources are needed.

## Slide 65: Funding Sources
Grants
  BUILD (Federal)
  Earmark (Federal/State)
  Building Resilient Infrastructure and Communities (Federal)
  Statewide Transportation Improvement Program (State)
  Federal Lands Access Program (Federal)
Local Options (Potential)
  System Development Charge
  Developer-built
  General fund
  Local Improvement District
  Special Road District
  Tax Increment Financing
Notes: BUILD – Better Utilizing Investments to Leverage Development
STIP – Statewide Transportation Improvement Program
FEMA BRIC – Building Resilient Infrastructure and Communities
FLAP (Federal Lands Access Program)
SDC – System Development Charge
LID – Local Improvement District
SRD – Special Road District
TIF – Tax Increment Financing

## Slide 66: How do Projects Get Done?
Smaller projects: County lead, use local funds if available
Major Projects:
  Identify possible funding sources, build coalition
  Refine the project, costs, and design
  Additional public outreach
  Multiple years to complete
Seek Grants: Some have more onerous requirements than others.
Opportunism: New grant opportunities, project underruns mean more $ for another project elsewhere, developer exactions
Developer: New development contributes to SDCs

## Slide 67: Next steps
Planning Commission TSP Hearing: September 24, 2025
Board of Commissioners Hearings:
  October 1, 2025
  October 15, 2025
Finalize TSP

## Slide 68: Thank you!